Section VI

Guidance/guidelines by source category: 
Source categories in Part III of Annex C

Part III Source category (m):
Waste oil refineries

Table of contents

VI.M	Waste oil refineries	1

1.	Introduction	1

2.	Waste oils	1

3.	Occurrence of polychlorinated dibenzo-p-dioxins and polychlorinated dibenzofurans (PCDD/PCDF) in used oils	2

4.	Waste oil refineries	2

4.1	Vacuum distillation + clay treatment	2

4.2	Vacuum distillation + chemical treatment	2

4.3	Hydrogen pretreatment + vacuum distillation	3

4.4	Thin film evaporation + extraction	3

4.5	Direct contact hydrogenation (UOP-DCH process)	3

5.	Measures for reduction of polychlorinated dibenzo-p-dioxins (PCDD), polychlorinated dibenzofurans (PCDF) and polychlorinated biphenyls (PCB)	3

6.	Conclusions	4

References	5

VI.M	Waste oil refineries

Summary

Waste oil refineries are listed in Annex C of the Stockholm Convention as a source that has the potential to form and release chemicals listed in Annex C.

For the purpose of this guidance section, waste oils (or used oils) are defined as any petroleum-based, synthetic, or plant- or animal-based oil that has been used. Waste oils may originate from two large sources: industrial waste oils, and vegetable and animal waste oils. Among the industrial waste oils, three main oil streams can be identified: industrial oil (e.g. hydraulic oil, engine lubricant, cutting oil); garage or workshop oil; and transformer oil.

Waste oils have been found to be contaminated with polychlorinated dibenzo-p-dioxins,, polychlorinated dibenzofurans and polychlorinated biphenyls.. At present there is no available evidence that polychlorinated dibenzo-p-dioxins and polychlorinated dibenzofurans or  polychlorinated biphenyls, are newly formed in waste oil refineries. The data available indicate that the polychlorinated dibenzo-p-dioxins and polychlorinated dibenzofurans or polychlorinated biphenyls released from waste oil refineries or waste oil handling and management plants are from industrial, intentional production of polychlorinated biphenyls or chlorobenzenes that are present in the waste oils either by contamination in the synthesis process (of these chemicals) or have become contaminated during the use phase or earlier recycling processes. In this sense, waste oil refineries represent a distribution source of chemicals listed in Annex C rather than a formation source.

According to available information, waste oil management options include reuse or regeneration; thermal cracking; and incineration or use as fuel. It should be noted that dumping and open burning are also practised in many countries.

For information on waste oil disposal in incinerators or on use as fuel, the relevant sections of this guidance document should be consulted (sections V.A Waste incinerators, V.B Cement kilns firing hazardous waste, VI.A Open burning of waste, VI.C Residential combustion sources, and VI.D Fossil fuel-fired utility and industrial boilers).

1.	Introduction

Waste oil refineries are listed in Annex C of the Stockholm Convention as a potential source of chemicals listed in Annex C. The information reported about waste oil refineries as sources of polychlorinated dibenzo-p-dioxins (PCDD) and polychlorinated dibenzofurans (PCDF) is very limited and further research is needed.

2.	Waste oils

Waste oils include any petroleum-based or synthetic oil that has been used. Water, chemicals, metal particles and dirt become mixed in with the oil during use, degrading its properties until it must be replaced by new oil.

New oils are a mixture of a base oil (mineral or synthetic) and additives (15–25%). The type of base oil and additives determine the possibility of regeneration and the possible formation of PCDD/PCDF in waste oil refineries.

3.	Occurrence of polychlorinated dibenzo-p-dioxins and polychlorinated dibenzofurans (PCDD/PCDF) in used oils

Hagenmaier and Brunner (cited by Fiedler) analyzed new and used (after 10,000 km in cars fuelled with leaded gasoline) motor oils. At a limit of quantification of 0.05 (g/kg per congener, no polychlorinated dibenzo-p-dioxins and polychlorinated dibenzofurans could be detected in fresh and used motor oils. However, highly chlorinated polychlorinated dibenzo-p-dioxins and polychlorinated dibenzofurans or were detected in recycled oils, probably from used oils contaminated with pentachlorophenol and its sodium salt, which in Europe were used in the mineral oil industry. It must

be noted that some of the additives used in modern lubricant oils contain chlorinated compounds and it is necessary to continue monitoring waste oils fed to refineries.

4.	Waste oil refineries

Waste oil refineries are designed to produce a base blending oil, some by-products and some wastes. The lighter parts of the by-products may be used as fuel; the heaviest, containing additives and carbonaceous species, may be used as a blending component in road surfaces.

Five technologies are representative of waste oil refineries:

4.1	Vacuum distillation + clay treatment

Water and		        H2SO4		 Clay + lime		  Light oil

light hydrocarbons

Base oil

Acidic and		    Acid oil

oily waste		    and clay

4.2	Vacuum distillation + chemical treatment

Water and	 	     Light components	 	 	 	H2

light hydrocarbons

Base oil

Heavy components

4.3	Hydrogen pretreatment + vacuum distillation

Water and	 		   H2		 		Light components

Light hydrocarbons

Base oil

Heavy components

4.4	Thin film evaporation + extraction

Water and		       Light components		  Solvent

light hydrocarbons

Base Oil

Heavy components	    Heavy components

4.5	Direct contact hydrogenation (UOP-DCH process)

5.	Measures for reduction of polychlorinated dibenzo-p-dioxins (PCDD), polychlorinated dibenzofurans (PCDF) and polychlorinated biphenyls (PCB)

As previously indicated, PCDD/PCDF and PCB in oil base or residue from waste oil refineries emanate from contaminated waste oils. Therefore, one basic measure to reduce PCDD/PCDF and PCB emissions from such refineries is to only treat waste oils with low PCDD/PCDF and PCB concentrations.

The European Re-refining Industry Association (Groupement Européen de l’Industrie de la Régéneration; GEIR) recommend that the following waste oils be preferred for regeneration:

Engine oils without chlorine;

Hydraulic oils without chlorine;

Non-chlorinated mineral diathermic oils.

6.	Conclusions

Waste oils have been found to be contaminated with PCDD, PCDF and polychlorinated biphenyls (PCB);

At present there is no available evidence that PCDD, PCDF and PCB are newly formed in waste oil refineries;

Waste oil refineries are a distribution source of chemicals listed in Annex C rather than a formation source;

The waste oil treated in waste oil refineries must have a low content of PCDD, PCDF, PCB and chlorinated additives.

References

Hagenmaier H. and H. Brunner. 1986. Bestimmung polychlorierter Dibenzodioxine und polychlorierter Dibenzofurane in Motorölen, Altölen und Zweitraffinaten. Fresenius Z. Anal.Chem.324, 23-26

Ruiz E. 1991. “Aceites Lubricantes para Motores a Gasolina.” In: Material del Curso de Educación Continuada: Fundamentos Básicos de Lubricantes. Bogotá, Colombia.

# Text boxes

Pretreatment

Acidification

Filtration

Distillation

Mixer unit

Hydrogen

Chemical treatment

Naphtha,

Gasoil

Vacuum distillation

Pretreatment

Vacuum distillation

Chemical treatment

Pretreatment

Flash seperator

Catalyst

section

Fractio-

nation

Heavy components

Base oil

Pretreatment

Thin film evaporation

Extraction